## Slide 1: Austrian experience in waste management
© iStockphoto.com/sodafish

## Slide 2
Waste Management Costs in Austria

## Slide 3: Costs of waste collection and transport
Chart: Costs in €/t
| Residual waste | Bulky waste | Biodegradable waste | Spent paper from HH | Spent glass | Plastic packaging | Metal packaging | HH-waste-like waste | Spent paper from Ind. | Cardboard | Construction site waste | Mineral aggregates
Datenreihe 1 | 110 | 110 | 105 | 124 | 70 | 320 | 310 | 60 | 72 | 142 | 35 | 8
HH= Households, Source: denkstatt 2009
Waste from households, schools, commerce < 240 l/week
Waste from industries
Fees for municipal waste management per household: + 100 €/a (2009)

## Slide 4: Treatment costs
Thermal treatment or mechanical-biological treatment of mixed household waste
  135 – 155/200 €/t
Composting, biogas from separately collected bio-waste:
  40 – 60 €/t
  Price situation for the incineration of waste oils and solvents in the Austrian cement industry: 50 - 100 € per ton (average, with a range of about up to € 160 paid for high quality waste oil and up to € 100 received for incineration of solvents) => MARKET PRICE1
  => Source separation is often cost efficient!
Source: denkstatt 2009

## Slide 5: Financing of MSW management
HH= Households, Source: denkstatt 2009

## Slide 6
Organising the
Waste Management System

## Slide 7: Waste Collection System Households (+commerce with ≤ 240 l/week)
 | Separate bins at house | Collection points | Civic amenity sites | Take back in shops
Residual waste | X |  |  | 
Paper | X | (X) | X | 
Biodegradable | X |  | X | 
Plastic packaging | X | (X) | X | 
Metal packaging |  | X | X | 
Glass |  | X | X | 
Textiles |  | (X) | X | 
Batteries |  |  | X | X
WEEE |  |  | X | X

## Slide 8: Collection Points

## Slide 9: Civic amenity sites

## Slide 10: Location of MBT and waste incineration plants
MBT
MBT
MBT
MBT
MBT
MBT
50
40
5
30
20
10
0
km
Waste incineration plant operating
Waste incineration plant planned/under construction
MBT
Mechnical-Biological-Treatment-(MBT)-Plant operating
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT-Plant planned/under construction
MBT

## Slide 11: Separate collection of household waste 2007
Recycables
Recycables(160 kg/cap):
80 % recycled
17 % used for energy recovery.
Household waste arisings:
167 kg/cap (37.4 %) residual waste
281 kg/cap (62.6 %) separately collected.
Chart: Shares in %
| Residual waste | Bulky waste | Hazardous waste | WEEE | Bio-waste | Paper | Glass | Plastics | Wood | Metals | Textiles | Other separately collected materials
Share in % | 37.3508 | 6.6338 | 0.62233 | 1.2125 | 18.4367 | 18.3911 | 5.3596 | 3.5892 | 4.2303 | 2.94 | 0.63306 | 0.60087
Source: Federal Waste Management Plan Statusbericht 2008

## Slide 12
Effects of integrated waste management on the generation of secondary waste

## Slide 13: Secondary wastes/required capacities for waste treatment
MSW-incineration: Slags and ashes ~1/3 of original volume, 10% of original weight
MBT: 30 – 40 % of input => landfill 30% => (co-) incineration
Recycling: in most cases at least 1 pre-treatment step is required
=> Less landfill capacity needed in an differentiated waste management, at the expense of additional other treatment capacities
Source: denkstatt 2009

## Slide 14: Recovery and Disposal Plants
Plant Type | Total Capacity in Mt/a 2005 | Number of Plants 2005 | Change till 2008
Sorting Plants | 1 | 123 | + 10
Municipal Solid Waste incineration | 1.7 | 9 | +1
Other Incineration | 2.9 | 180 | +7
Mechanical-Biological Treatment (MBT) | 0.8 | 16 | +1
Composting + Biogas | 1.4 | 780 | Composting + 13
Physical-Chemical Treatment | 0.5 | 37 | +0
Treatment of Construction Waste | 5.5 | 293 | +48
Landfills |  | 666 | -118
Special Treatment + Recycling | 2.4 | 190 | 
Source: Federal Waste Management Plan 2006, Statusreport 2008

## Slide 15: Location of MBT and waste incineration plants
MBT
MBT
MBT
MBT
MBT
MBT
50
40
5
30
20
10
0
km
Waste incineration plant operating
Waste incineration plant planned/under construction
MBT
Mechnical-Biological-Treatment-(MBT)-Plant operating
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT
MBT-Plant planned/under construction
MBT

## Slide 16
Overall picture of hazardous waste management – combination of different treatment methods (schematic picture)

## Slide 17
Costs and Benefits of Remediation of contaminated sites, and effects on the waste management sector

## Slide 18: Remediation of contaminated sites as source for secondary waste
 |  | Remediation of Contaminated sStes |  | 
 | Landfilled Waste (Total) | Excavated contaminated material | of which landfilled | % of total landfilled waste
 | [Mio. t/a] | [Mio. t/a] | [Mio. t/a] | 
1998 | 7 | 1 | 0,8 | 11%
1999 | 6 | 0,9 | 0,2 | 3%
2000 | 7,9 | 0,5 | 0,3 | 3%
2001 | 7,5 | 0,1 | 0 | 
2002 | 8,6 | 1,7 | 1,2 | 14%
2003 | 10,5 | 4,5 | 3,1 | 29%
2004 | 9,7 | 0,7 | 0,7 | 8%
Sum (7 years) | 57,2 | 9,4 | 6,2 | 10%
Source: Remediation of contaminated waste in Austria (Umweltbundesamt and KPC, 2007)

## Slide 19: Effects of remediation of contaminated sites on the Austrian waste management sector
In the last years,
1% of total waste generation (+/- 50 Mio. t/y) and
6% of total excavated material, mostly soil (+/- 20 Mio. t/y)
stem from remediation of contaminated sites.
10% of total landfilled waste is secondary waste from remediation.

## Slide 20: Costs of remediation of contaminated sites - financing
The fund for remediation of contaminated sites was established in 1989. Since then ~ 150 sited were remediated.
The fund spends in average 50 Mio €/y for project funding, of which 35% go to the waste management sector and 45 % to the construction sector.
For ~50 % of remediation projects, the remediation method was excavation and disposal of the material as waste.

## Slide 21: Costs and financing of remediation
Source: Remediation of contaminated waste in Austria (Umweltbundesamt and KPC, 2007)

## Slide 22: Contact & Information
Brigitte Karigl
+43 1 31304 5568
brigitte.karigl@umweltbundesamt.at
Umweltbundesamt www.umweltbundesamt.at
Green Serbia Belgrade■ 29.2.2012